Date of publication MMM-22, yyyy, date of current version MMM-dd, yyyy.
www.computingonline.net / computing@computingonline.net
Print ISSN 1727-6209
Online ISSN 2312-5381
DOI 10.47839/ijc.19.3.XX
Designing Microcontroller
 module with target to use
AVR/PIC assembler
Veselin Stanchev , Eng. MSc1

1Department ICT, Technical University-Plovdiv Branch, Plovdiv, Bulgaria
Corresponding author: Veselin Stanchev , Eng. Msc (e-mail: vrstanchev@tu-plovdiv.bg).

 ABSTRACT Assembly languages are very useful for programming of micro-controllers, microprocessors, embedded devices, real-time operating systems. The most natural way for micro-controller programming is to use Assembly languages. For different types of micro-controller families - AVR/PIC-based, there are different assembly languages. For AVR-based micro-controllers such as - ATtiny13,ATtiny85,ATMega32u4 different assembly languages can be used – AVR Assembler or GNU Assembler. Micro-controllers can be used for micro-controller modules design. This paper describes design and programming of micro-controller module which uses both AVR-based and PIC-based micro-controller. This module can be used for educational purposes. It shows communication between its micro-controllers.

 KEYWORDS PCB; MCU; AVR/PIC; Assembly language; Micro-controller module

INTRODUCTION Usage of free assembly languages is very important for understanding Computer Architectures. Free assembly languages can be used for university purposes. To explain usage of them for micro-controllers, micro-controller boards can be designed using open-source EDA software such as: Fritzing or LibrePCB. On single micro-controller board can be used micro-controllers together.

They are several variants for that – usage of PIC-based micro-controllers, usage of AVR-based micro-controllers or AVR/PIC micro-controllers together. Target of the current project is to use AVR assembler and PIC assembler through custom communication protocol. There are requirements for hardware and software part of the project. ATtiny85 and PIC10F320 are chosen.

For software part of the project are used tools such as: Git, GNU Make, GNU GCC, GNU PIC Utils, avra. Git is used for project version-control. GNU Make is used for automatization of software build. Software of the project is also produced as static Assembly library.

Hardware part is created by using of LibrePCB. LibrePCB is used for schematic design, footprints of micro-controllers and layout of the micro-controller module.

MATERIAL AND METHODS Project orientation is fully practical. The micro-controller module can be used for university purposes. For realization of the project are used open-source tools. Because of that project can be upgraded easily. The project can be used for: assembly language labs, micro-controller labs, understanding of micro-controller communication, understanding of AVR/PIC programming.
Existing micro-controller modules ANAVI MACRO PAD 2, ANAVI LIGHT CONTROLLER, Raspberry Pi Pico and AVR64DD32 Curiosity Nano. For each of them are analyzed: supported micro-controllers, supported communication protocols, supported interfaces, supported assembly languages.
Example: ANAVI MACRO PAD 2 and ANAVI LIGHT CONTROLLER.

        Figure 1. ANAVI MACRO PAD 2 Figure 2. ANAVI LIGHT CONTROLLER
Requirements of the project are hardware-based and software-based. For hardware-based requirements: AVR/PIC-based micro-controllers has to be chosen. ATtiny85 and PIC10F320 are chosen.

        Figure 3. ATTiny85 Figure 4. PIC10F320
Micro-controller’s features are analyzed. ATTiny85 has 8kb flash memory, 8-bit timer,

For design of micro-controller module LibrePCB is chosen. AVR/PIC-based micro-controller’s symbols are created. Footprints for them are created.

        Figure 5. Symbol of ATTiny85 Figure 6. Footprint of ATTiny85

        Figure 7. Symbol of PIC10F320 Figure 8. Footprint of PIC10F320

USB interface is chosen for power and programming. So micro-controller module block diagram is created

Figure 9. Micro-controller module block diagram

Due to chosen micro-controllers , interfaces and block diagram micro-controller module’s schematic is created.

Figure 10. Micro-controller module schematic

Bev

References
Reference to a journal publication:
[1]	J. van der Geer, J.A.J. Hanraads, R.A. Lupton, “The art of writing a scientific article,” Journal of Science Communication, vol. 16, issue 3, pp. 51-59, 2000.

Reference to a book or a report:
[2]	W. Strunk Jr., E.B. White, The Elements of Style, third ed., Macmillan, New York, 1979, 350 p.

Reference to a chapter in an edited book:
[3]	G.R. Mettam, L.B. Adams, How to prepare an electronic version of your article, in: B.S. Jones, R.Z. Smith (Eds.), Introduction to the Electronic Age, E-Publishing Inc., New York, 1999, pp. 281-304.

Reference to a conference proceedings:
[4]	C.-H. Lin, J.-C. Liu and C.-W. Liao, “Energy analysis of multimedia video decoding on mobile handheld devices,” Proceedings of the International Conference on Multimedia and Ubiquitous Engineering, Seoul, Korea, April 26-28, 2007, pp. 120-125.

Online publication:
[5]	M. Shell, The IEEEtran.cls Package, 2007, [Online]. Available at: http://www.ctan.org/tex-archive/macros/latex/contrib/IEEEtran/

Veselin Stanchev Graduate Eng. Master of Science. / Professional Field: Computer Systems,Complexes and Networks / Scientific field: Computer Architectures